## Slide 1
FYP PROPOSAL DISCUSSION
Tactile Calligraphy Robot
Making brush–paper interaction
measurable and controllable
Notes: Introduce the project in one sentence: the goal is not only to replay an XY path, but to sense brush deformation and control contact during writing.
[Sources]
- FYP_Proposal_Discussion_2026.pptx (project photograph and context)

## Slide 2
BACKGROUND
Calligraphy depends on
contact, not path alone
PRESSING + LIFTING
change brush shape, stroke width
and ink distribution.
ROBOT
LIMITATION
A fixed XY–Z path
cannot observe or correct
changes in brush contact.
The missing variable is
brush–paper interaction.
02
Notes: Explain the background with a simple contrast. Calligraphy depends on continuous pressing and lifting. The robot can follow a path, but without contact sensing it cannot tell whether the brush is behaving as intended.
[Sources]
- plan.md (project goal and position-only limitation)

## Slide 3
IMPORTANCE
Why this project matters
01
Repeatability
Control contact so the same plan produces more consistent strokes.
02
Embodied skill
Capture pressing and lifting—not only the final ink trace.
03
Transferable robotics
A testbed for compliant tools, soft sensing and contact control.
03
Notes: Emphasise three reasons the project matters: improving repeatability, preserving the dynamic pressing-and-lifting part of calligraphy, and developing a reusable approach for robots that manipulate soft or deformable tools.
[Sources]
- plan.md (project objective and proposed tactile control scope)

## Slide 4
PROPOSED
CONTRIBUTION
The tactile loop
is built into
the brush
1
Embedded sensing
Magnetic field tracks brush deformation.
2
Contact estimate
Calibrated ΔB becomes a contact target.
3
Tactile feedback
Vertical motion adapts during execution.
StrokePlan links demonstration data to robot execution.
04
Notes: Present these as the proposed contributions, not as a claim of being the first in the world. The key difference is that sensing is embedded close to contact, the signal becomes a control target, and StrokePlan connects demonstration with execution.
[Sources]
- plan.md (interfaces g_meas and StrokePlan)
- docs/professor-intro.md (system concept)

## Slide 5
CURRENT
PROGRESS
Sensing
Live three-axis magnetic readout and USB recording at approximately 100 Hz.
Data
A preliminary V0 dataset has been collected and checked for timing.
Execution
Open-loop robot writing and the control/runtime software are available.
Still to prove: an assembled brush driving a real robot closed loop.
05
Notes: Keep the progress summary brief. The sensor and recorder work, preliminary data exists, and the robot execution side has been demonstrated. The complete assembled sensor-driven hardware loop is still the next proof.
[Sources]
- plan.md (A1 and A3 status)
- data/sensor/delta_b/delta_b_v0_manifest.md
- docs/z-control.md (control software evidence)

## Slide 6
MY NEXT WORK
Build the brush. Validate the signal. Prove the loop.
Goal: one repeatable real-world closed-loop writing comparison.
01
Integrate the sensor
Dry-fit, bond and record insertion geometry and cable routing.
02
Characterise the signal
Test noise, response, return-to-zero, hysteresis and lateral drag.
03
Close the loop
Calibrate ΔB to depth, synchronise ΔB + XY, then compare fixed-z and feedback.
06
Notes: First I will complete physical brush integration. Next I will validate whether the assembled signal is stable and separable. Finally I will calibrate it, synchronise it with motion data, and compare open-loop with tactile-feedback writing.
[Sources]
- plan.md (A0–A4 next tasks and gate experiments)

## Slide 7
PROPOSAL
FOCUS
ONE
CREDIBLE
RESULT
Core deliverable
An assembled tactile brush,
a calibrated signal and
feedback-controlled writing.
Learning-based generalisation comes after the physical loop is proven.
07
Notes: Close by asking for scope confirmation. The proposal should first prove a real tactile loop. Learning-based generalisation should remain a later extension rather than compete with the core hardware validation.
[Sources]
- plan.md (core-first scope and later learning-based milestones)